## Slide 1
Afrodite Sevasti, GÉANT/GRNET
Activity Leader for eInfrastructure Integration
Digital Infrastructures for Research event
The GÉANT-CSP integration use case
eInfrastructure interoperation approach and developments
28-30th September 2016

## Slide 2: eInfrastructure interoperation In this talk...
Federated identity management
Governance
Business and operational interoperation

## Slide 3: The drive for interoperation Forecasts and expectations
eInfrastructure user base
  1,000s of campuses and institutions
  1,000,000s of users
Multiple levels of user relations
Evolving user community requests
  On-demand delivery
  Minimum lead times
  One-stop-shop
  Service bundling/composite services
A European scale environment
Demand for eInfrastructure services
Requirements for both eInfrastructure and commercial services
Notes: The infrastructure layer of the ECI should be ready to handle the increasing demand in volumes and capabilities

## Slide 4: Digitizing European Industry European Cloud Initiative
“How to better connect the new and existing infrastructures across Europe?”
European Data Infrastructure
  Super-computing capacity
  Fast connectivity
  High-capacity cloud solutions
Challenges
  Fragmentation (domains and countries)
  Governance
  Disconnection
  Silos
The high-bandwidth networks & supercomputing capacity to access & process large datasets stored in the Cloud
Notes: ECI to better connect and enable federation of infrastructures across Europe (from intro section)
There is an infra layer and it is fragmented
This needs to be fixed
Data not there as the focus is on the infrastructure layer
The presentation will focus on three out of the four challenges

## Slide 5: A shared high-speed connectivity substrate
NREN
OpenAIRE
Regional
NREN
European RIs
Cloud Service Provider (PoPs)
Notes: Forthcoming GEANT service era
Getting very complex for GEANT/NRENs
Requests from individuals, labs, VROs, campuses
Different kinds of SPs connected
Demos have been done on things like OCX (including CSPs)
Indicative, not happening today, but we need to be prepared
Getting more complex to coordinate and orchestrate
Users getting more demanding in terms of capabilities and lead times

## Slide 6: Accessing Cloud Service Provider resources
How/when is my traffic steered to my pool of VMs?
When does charging start?
Who do I turn to in case of performance incidents?
What is the guaranteed uptime of my service?
How can I dynamically update my services?
NREN
NREN
Cloud Service Provider (CSP)
CSP
CSP
SERVICE =
VMs + network access
CSP Portal

## Slide 7: NREN service stack for CSP services’ delivery
Infrastructure/
network connectivity provider(s)
Cloud VM provider
Composite service offering requires business-to-business and operational interoperation

## Slide 8: IP access to CSP resources Solution at the data plane (*)
GEANT CLOUD VRF
NREN
PEERING REN
IX
NREN
BGP announcements
No tag
NREN tag
Cloud Provider tag
CSP
CSP
CSP
BGP-based routing overlay
(*) figure by E. Capone, GEANT Ltd.

## Slide 9: L2 private access to CSP resources Solution at the data plane
NREN
Primary (& backup) provider L2 VPNs
S-VLAN tag
Utilizing different technologies across domains
‘CSP order ID’ and ‘S-VLAN’
Primary & backup customer circuits
C-VLAN tag
CSP portal
S-VLAN provides the service ID at the physical connection point
End-to-End QinQ

## Slide 10: User expectations
One-stop shop for cloud and connectivity services
Clear indication of status for VM and e2e connectivity orders and live services
Visibility to business operations
  Is my institution eligible to service?
  What is the status of my order?
  Can I upgrade my service?
  I wish to submit a service incident
Visibility to service health and operations
  What is the connectivity throughput to my VM?
  What is the current utilization of my VM?
  When is the next scheduled maintenance for my service?
  What has been the uptime for my service for the past 3 months?
CSP portal
NREN
?

## Slide 11: Short-term plan: ‘two-stops’ shop
Cloud SP portal
Order VMs
Select network connectivity provider -> GEANT
Retrieve ‘CSP Service ID’ and ‘S-VLAN’
Network connectivity one-stop-shop portal
Insert institution, CSP and ‘CSP Service ID’ information
Insert S-VLAN information
Order e2e L2 VPN to VMs
NREN
Orchestration
Step 1
Step 2
Network service providers - NSPs
CSP

## Slide 12: Long-term plan: one-stop shop
C2B and B2B interactions
R&E Cloud Services one-stop-shop portal
Authenticate in institution via eduGAIN
Select CSP
(CSP catalogue retrieved) order VMs
(Network services catalogue retrieved) order L2 link
Use dashboard to manage/monitor service
Orchestration
2
4
Dynamically populated GÉANT Cloud Service Provider Catalogue
Catalogue offerings of the selected CSP
Network services catalogue offerings (e.g. L3 connectivity, L2 VPN)
Invoke CSP API or B2B interfaces for order management & provisioning
Invoke NSP API or B2B interfaces for order management & provisioning
Invoke CSP/NSP API or B2B interfaces for monitoring and service management
1
NREN
3
5
6
NSPs
CSP

## Slide 13: What is the orchestrator?
A workflow engine exposing a service bus for external communications
  SP interactions are implemented as services
Controls party interactions and implements e2e service delivery and management logic
  Different workflows can be defined for different services or business agreements
Orchestrators can be deployed either:
  in a centralized mode (e.g. a single orchestrator overarching campus, NREN, GEANT network SPs) or
  in a distributed mode: each SP deploys a workflow engine that supports east-west interactions with peering SPs
GEANT is working on an open-source reference implementation of an orchestrator+service bus solution

## Slide 14: Network and Cloud SP: Fulfilling orders
Each R&E cloud service order is being decomposed by the receiving orchestrator:
  VM resources order dispatched to the CSP
  e2e connectivity order can be further decomposed per NSP
Either the orchestrator or the NSP can receive the e2e connectivity service order
Then invoke the required B2B transactions between NSPs to fulfill the order
  NSPs that expose B2B interfaces communicate directly and minimize interaction with the orchestrator
  All other NSPs (non B2B-capable, supporting manual provisioning) communicate via the orchestrator
any

## Slide 15: Network and Cloud SP: B2B operations
Federated service management
Catalogue information exchange
  Common baseline Network Service Descriptors – e.g. TOSCA NSD
Resource topology/reachability information exchange – e.g. NSI DDS*
Provisioning – common Order State semantics
Service lifecycle management – common Service Lifecycle semantics
Ticketing – common Trouble Ticketing semantics – e.g. Trouble Ticket APIs
  Incident management
SLA monitoring and negotiation
  Common baseline SLA models/descriptors
Accounting/billing
any
Service/resource programmability
*Document Distribution Service

## Slide 16: Adopting standards Application Programming Interfaces
Operations Management Interfaces
  Catalog to Catalog Interface
  Service Ordering & Activation
  Service Quality Management
  Performance
  Fault Management
  Inventory
  Resource Order
  Policy Information Exchange
  Security
  …..
Global Digital Marketplace

## Slide 17: A flexible model Opt-in interoperability
Orchestrator-invoked interfaces
No automation required
Basic information exposed via RESTful APIs towards the orchestrator
Notifications via emails, ticketing system etc.
B2B/operational interfaces
Orchestration entry points (e.g. URIs)
Advertising catalogue
Resource topology
Order Management & Provisioning
Service Lifecycle Management
Operations (Monitoring, Troubleshooting, SLAs)
Accounting/billing
Orchestration
NREN
CSP
NSPs
User-demand as an incentive for automation

## Slide 18: Network connectivity provisioning Technologies at GÉANT/NRENs
Orchestration
NSPs
NSI-capable NSPs
IX
NREN
Network Services Agent (NSA)
BoD cloud
MDVPN fabric (*)
EVPN /DCI fabric (*)
(*) see presentation from X. Jeannin in 8B
Orchestration
NREN
NSPs
NREN
IX
Orchestration
NREN
Data center
Data center
IX

## Slide 19: An eInfrastructure interoperation scenario
Orchestration
NREN
NSPs
PaaS orchestrator
IaaS/PaaS providers expose selected orchestration capabilities
Request for inter-domain/WAN services via agreed Network Service Descriptors (e.g. TOSCA)
All other B2B interactions are possible
  Opt-in applies again
GÉANT/NRENs serving as specialized/on-demand network service providers for all eInfrastructures
TOSCA NSD
Orchestration with WAN connectivity services

## Slide 20: A business case for GÉANT/NRENs
GÉANT-Microsoft partnership for ExpressRoute offering:
Institutions to extend their on-premises network into the Microsoft cloud over dedicated private connections
More CSPs, more IaaS services

## Slide 21: GÉANT’s Pan-European tender for IaaS services Multi-provider interoperability is inevitable
Portfolio of services and joint cloud delivery and adoption
NRENs bring the portfolio to their Institutions to consume
Participating CSPs
  Amazon (through resellers)
  Cloudsigma
  Dimension Data
  Interoute
  itSoft
  KPN
  Lattelecom
  Microsoft (through resellers)
  NTT Europe
  T-Systems
  Telecom Italia
  Vancis​
Concluded within September

## Slide 22: Conclusions
GÉANT/NRENs challenged to join the global IT services marketplace
Orchestrated solution underway
  For the GEANT/NREN-Microsoft Azure ExpressRoute offering
  Modular, opt-in approach
  Standards-based interfaces and B2B interactions
Fully reusable for eInfrastructure integration
  Open to collaborations
Complementarity with on-going efforts
  eInfrastructure service catalogues
  Federated service management
If you cannot fully automate then…. orchestrate !

## Slide 23
sevasti@grnet.gr